## Slide 1: Internet Protocol Version 6
Course Code: COE 3206
Dept. of Computer Science
Faculty of Science and Technology
Course Title: Computer Networks
Lecturer No: |  | Week No: |  | Semester: | 
Assistant Professor: | Dr. Mousumi Bala; mousumi.bala@aiub.edu |  |  |  | 

## Slide 2: Lecture Outline
To introduce the IPv6 addressing scheme and different notations used to represent an address in this version.
To explain the three types of addressing used in IPv6: unicast, anycast, and multicast.
To show the address space in this version and how it is divided into several blocks.
To discuss some reserved blocks in the address space and their applications.
To define the global unicast address block and how it is used for unicast communication.
To discuss how three levels of hierarchy in addressing are used in IPv6 deploying the global unicast block.
To discuss auto configuration and renumbering of IPv6 addresses.

## Slide 3: Measurement of 128 bit
Examples:
2001:0211:00AB:0000:0000:0000:0000:0001
Working in the 1st Hexted we can see
2 = 0010 (4-bit)
0 = 0000 (4-bit)
0 = 0000 (4-bit)
1 = 0001 (4-bit)
----------------------------------------
= Total 16 bit in One Hexted.
In total :- 16 bit * 8 Hexted = 128 bit.

## Slide 4: How to Shorten IPv6 Address
Leading Zero Can be Omitted.
Consecutive Hexted of Zeros can be represented/replaced by double colon (::).
Double colon can only be used once in an IPv6 Address.
2001:0211:00AB:0000:0000:0000:0000:0001
  =According to the rules, we can write
      2001:211:AB:0:0:0:0:1 -Leading 0’s are omitted
      2001:211:AB::1 - Consecutive 0 means (::)
      Already Used one double colon.
  Final Shorten IP address:-
2001:211:AB::1

## Slide 5: Problem set
Show the unabbreviated colon hex notation for the following IPv6 addresses:
a. An address with 64 0s followed by 64 1s.
b. An address with 128 0s.
c. An address with 128 1s.
d. An address with 128 alternative 1s and 0s.
Solution:-
a. 0000:0000:0000:0000:FFFF:FFFF:FFFF:FFFF
b. 0000:0000:0000:0000:0000:0000:0000:0000
c. FFFF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF
d. AAAA:AAAA:AAAA:AAAA:AAAA:AAAA:AAAA:AAAA

## Slide 6: Problem set (cont…)
Show abbreviations for the following addresses:
a. 0000:0000:FFFF:0000:0000:0000:0000:0000
b. 1234:2346:0000:0000:0000:0000:0000:1111
c. 0000:0001:0000:0000:0000:0000:1200:1000
d. 0000:0000:0000:0000:0000:FFFF:24.123.12.6
Solution
a. 0:0:FFFF::
b. 1234:2346::1111
c. 0:1::1200:1000
d. ::FFFF:24.123.12.6

## Slide 7: Types of ipv6 Address

## Slide 8: Types of ipv6 Address (cont…)

## Slide 9: What is removed in ipv6

## Slide 10: Convert IPv4 to IPv6
First 8 bits 0, following 88 bits will also be zero, last 32 bits will be the IPv4 address.
IPv4 address: 192.168.10.62
Convert it into IPv6
Representing each octet with 8 bits binary:
192 = 1100 0000 = C0
168 = 1001 0100 = 94
10 = 0000 1010 = 0A
62 = 0011 1110 = 3E
IPv6 address will be 0:0:0:0:0:0:C094:0A3E  ::C094:A3E

## Slide 11: IPv6: Link Local to MAC Link Local Address
All the link local address starts with FE80
It is used for retrieving MAC address
FE80::5D39:84FF:FE29:3064
5D39:84FF:FE29:3064
Rules to convert link local into MAC Address:
i) Drop the First four Hextets
ii) Flip the 7th bit of 5th Hextet
iii) Drop the 2nd Octet of 6th Hextet
iv) Drop the 1st Octet of 7th Hextet
FE80::5D39:84FF:FE29:3064
drop flip drop
5D39=0101110100111001
7th bit flip 5F39
MAC address: 5F39:8429:3064

## Slide 12
References
  Data Communications and Networking, B. A. Forouzan, McGraw-Hill, Inc., Fourth Edition, 2007, USA.
  https://www.geeksforgeeks.org/basics-computer-networking/
  https://www.tutorialspoint.com/computer_fundamentals/computer_networking.htm

## Slide 13
Books
  Data Communications and Networking, B. A. Forouzan, McGraw-Hill, Inc., Fourth Edition, 2007, USA.
  Computer Networking: A Top-Down Approach, J. F., Kurose, K. W. Ross, Pearson Education, Inc., Sixth Edition, USA.
  Official Cert Guide CCNA 200-301 , vol. 1, W. Odom, Cisco Press, First Edition, 2019, USA.
  CCNA Routing and Switching, T. Lammle, John Wily & Sons, Second Edition, 2016, USA.
  TCP/IP Protocol Suite, B. A. Forouzan, McGraw-Hill, Inc., Fourth Edition, 2009, USA.
  Data and Computer Communication, W. Stallings, Pearson Education, Inc., 10th Education, 2013, USA.